## Slide 1
Secure boot and firmware update
Architecture options for OEMiRoT on STM32C5
based on example_oemirot_dualslot_hwcrypto

## Slide 2
The vocabulary, in one slide
Every term this deck uses. Worth leaving on screen during questions.
THE PIECES
RoT
Root of Trust — the small immutable bootloader
that runs first and checks everything else
Image
firmware + a header + metadata. Not a bare .bin
Slot
a flash region sized to hold exactly one image
TLV
Tag-Length-Value — the variable-length records
appended after the firmware: hash, signature,
version, dependencies
Magic trailer
16 bytes at the end of the download slot meaning
"a candidate is ready"
Confirm flag
the new firmware's "I booted, keep me" mark (swap
mode only)
THE PROTECTIONS
OB
Option Bytes — chip configuration stored outside
the firmware: boot address, protections, lock bits
WRP
Write Protection — flash pages that cannot be
erased or written. Makes the RoT immutable
HDP
Hide Protection — a region that disappears from
the memory map once the RoT hands over
RDP
Readout Protection — how much a debug probe may
see. 0 = everything, 2 = nothing, permanently
MPU
Memory Protection Unit — the CPU's runtime rules
on what may be read, written or executed
NV counter
a non-volatile counter that only ever increases —
the anti-rollback floor
THE CRYPTOGRAPHY
SHA-256
the hash — a short fingerprint of the image
ECDSA P-256
the signature scheme — proves the image came from
whoever holds the private key
AES-128-CTR
the cipher that scrambles the payload
ECIES
how the AES key is wrapped so that only this
device can unwrap it
PKA · SAES · HASH
the hardware engines that run the three above
XIP
eXecute In Place — the CPU runs code straight from
flash, with no copy to RAM
YModem
the serial file-transfer protocol used here to
move an image onto the device
TPC
STM32TrustedPackageCreator — the tool that signs
and encrypts the image
Notes: Vocabulary slide. Do not read it out - put it up, say it stays available, and come back to it whenever someone asks what a term means.

## Slide 3
Secure boot: two stages, one door that only opens forwards
OEMiRoT verifies the application on every reset — then hides itself before handing over
RESET
BOOTADD
OEMiRoT — immutable root of trust
1
Apply protections
MPU · tamper · ECC · caches
2
Check option bytes
BOOTADD · BOOT_LOCK · WRP · HDP · RDP
3
Verify the application
SHA-256 + ECDSA P-256, twice (fault-injection hardened)
4
Close the door
shrink MPU · close HDP · disable crypto clocks
verified
jump
APPLICATION
0x08018400
updatable firmware
carries the update agent
After the jump the RoT code and the keys are GONE from the map (HDP).
The application cannot read them, cannot call back, and cannot modify the boot stage. Only a reset returns to the RoT.
Immutable — write-protected (WRP)
Hidden after boot (HDP)
Re-verified on every reset
Any failed check ends at Error_Handler — the application simply never runs.
Notes: The frame for everything else: an immutable first stage that checks the second one, then hides itself. Nothing the application does can reach back into it.

## Slide 4
How the device knows the firmware is yours
Signing proves who made it · encryption stops anyone reading it · they are independent choices
What an image actually is
HEADER
0x400
ENCRYPTED PAYLOAD
your firmware
TLVs
hash · signature · version · dependencies
IN THE FACTORY (offline)
signing PRIVATE key
never leaves — if it leaks, every device is lost
encryption key (ECIES P-256)
scrambles the payload with AES-128
one key pair today — no revocation path
and the bootloader is immutable, so it cannot be added later
ON THE DEVICE (0x12000, hidden by HDP)
SHA-256 of the public key (32 bytes)
not the key itself — the image carries that, and the hash proves it
decryption key — raw in flash
readable by anyone who defeats RDP and HDP
stronger option: keep it inside SAES hardware
so the usable key never exists in readable memory
When the decryption actually happens — twice, both inside the bootloader — is the next slide.
Two questions people mix up:
"Is this firmware really from us?" → SIGNING. Without it, anyone can install anything.
"Can a competitor read our firmware?" → ENCRYPTION. Optional — drop it and one key leaves the device.
Notes: Signing and encryption answer different questions. Note the two weak points we own: a single key pair with no revocation path, and a decryption key sitting raw in flash.

## Slide 5
When exactly is the image decrypted?
Twice — both times inside the bootloader, both during one install. Never afterwards.
FACTORY
1
sign the PLAINTEXT first,
then encrypt the payload
the AES key is wrapped
with ECIES into a TLV
no decryption
›
DOWNLOAD
2
the app writes bytes
it cannot read
secondary slot
= ciphertext
no decryption
›
VERIFY CANDIDATE
3
decrypt block by block
IN RAM while hashing —
the signature covers the
plaintext. Nothing written.
DECRYPT — pass 1
›
INSTALL
4
decrypt while copying
into the primary slot.
This one persists:
plaintext lands in flash.
DECRYPT — pass 2
›
EVERY BOOT AFTER
5
primary slot is plaintext:
hash it directly, or skip
via the hash reference.
Runtime: crypto clocks off.
no decryption
before pass 1: unwrap the AES key with the ECIES private key
Why twice, and not once?
Verification must finish BEFORE installation starts.
Pass 1 is throwaway — it only reconstructs the hash.
Install-then-verify would let a forged image overwrite
your working firmware before you discovered it was bad.
Where plaintext exists
secondary slot
never — ciphertext from download until install
primary slot
always, once installed — this is what the CPU runs
RAM
transiently, block by block, during passes 1 and 2
SWAP mode adds a third pass: the outgoing image is RE-ENCRYPTED on its way into the secondary slot.
Encryption protects the image in transit and while it is staged. The installed image sits in flash as plaintext — what protects it there is RDP and WRP.
Notes: Answers 'when is it decrypted'. The headline: twice, both inside the bootloader, both during one install, never afterwards. The 'why twice' box is the part people ask about - verification must finish before installation starts.

## Slide 6
Where everything lives — 1 MB of flash
STM32C5A3ZG · two 512 KB banks · 8 KB pages · offsets from flash_layout.h
RoT code
PRIMARY SLOT
the firmware that runs
SECONDARY SLOT
download area
0x00000
0x18000
0x8C000
0x100000
bank 1 | bank 2
72 KB
464 KB
464 KB
WRP — cannot be erased or written
HDP — invisible once the application runs
the 24 KB the RoT keeps for itself
0x12000
keys
hash of the signing public key + the decryption key
0x14000
counters
anti-rollback floor — refuses older firmware
0x16000
hash refs
lets a known-good image skip the signature check
Why the primary slot crosses
the bank line
96 KB comes off the front for the RoT, so
splitting the remaining 928 KB in half lands
96 KB past the 0x80000 midpoint. Aligning
to the bank instead would mean 416 KB
slots — 48 KB less in each.
Harmless for the install — it bites RWW and bank swap.
Two slots of the same size is what makes a safe update possible — and it is why the app budget is 464 KB, not 925 KB.
Notes: Real offsets from flash_layout.h. The headline number is 464 KB usable out of 1 MB - that is the price of the second slot, and it drives most of the later decisions.

## Slide 7
From build to running firmware
The bootloader never downloads anything — it only ever looks at flash after a reset
IN THE FACTORY
private keys never leave
IN THE FIELD
any transport you like
ON THE DEVICE
the only place trust is decided
1
Build
appli.hex — plain firmware
2
Sign and encrypt
prepend a 0x400 header
encrypt the payload (AES-128)
append signature TLV (ECDSA P-256),
version, security version, hashes
appli_fwu_enc_sign.bin
safe to publish — it is encrypted and signed
3
Deliver
YModem here —
BLE, USB, Ethernet
would work the same
4
The app stages it
erase the secondary slot, write the image into it
5
The app asks for it
write the magic trailer at the end of the slot
6
Reset
7
The RoT decides
unwrap the key · verify (decrypting to hash)
install (decrypting) · verify again · run it
Why this split matters: all the network code lives in the replaceable application.
The immutable part stays small, offline, and has no attack surface facing the outside world.
Notes: Key point: the bootloader never downloads anything. All transport code lives in the replaceable application, so the immutable part stays small and offline.

## Slide 8
What the bootloader does on every single reset
Three ways to be rejected — and nothing runs until the signature checks out
RESET
Apply protections, check option bytes
MPU · tamper · WRP · HDP · RDP · boot address
mismatch
Chip not in the expected state
someone changed the option bytes — halt
Is an install requested?
magic trailer at the end of the secondary slot?
yes
Verify the candidate
decrypt to hash · signature · version ≥ floor · dependencies
fail
Candidate refused
forged, corrupted or too old — the old image keeps running
INSTALL
overwrite · swap · bank flip — see the next slides
Verify what sits in the primary slot
hash reference matches? skip · otherwise verify in full, twice
fail
Nothing runs
a tampered primary slot is never executed
Close HDP · disable crypto · JUMP
no
the ordinary boot —
no update pending
Notes: This runs on every reset, not just on update. Three independent rejection paths, and the primary slot is re-verified even when no update is pending.

## Slide 9
Dual slot, OVERWRITE — what runs on the board today
The new image is copied over the old one. Simple, power-fail safe, and there is no way back.
1
The app erases the download area
PRIMARY SLOT
RUNNING
SECONDARY SLOT
ERASED
2
YModem writes the new image into it
PRIMARY SLOT
RUNNING
SECONDARY SLOT
STAGED — not trusted yet
3
The app writes the magic trailer
PRIMARY SLOT
RUNNING
SECONDARY SLOT
STAGED — not trusted yet
MAGIC @ 0xFFFF0
4
Reset — the RoT verifies (decrypting to hash), then copies (decrypting)
PRIMARY SLOT
COPY IN PROGRESS
SECONDARY SLOT
STAGED — not trusted yet
5
Done — the old firmware no longer exists
PRIMARY SLOT
RUNNING
SECONDARY SLOT
inert copy
Power loss is safe
The magic trailer is still set,
so the copy simply starts again
at the next boot. The device
cannot be bricked mid-install.
The one it cannot fix
A correctly signed image that
installs, boots, then crashes.
The old firmware is gone and
the update menu lived inside
the app — so nothing can
recover it but a probe.
Forged, corrupted or out-of-date images are rejected at step 4 — before anything is overwritten.
Notes: What the board does today. Walk the five states, then land on the red box: a signed image that crashes takes the update path down with it.

## Slide 10
Why the application has to ask, explicitly
Step 3 of the update sequence — the one that looks redundant
The two stages cannot talk to each other.
The RoT runs, hands over, and closes HDP behind it.
No call back. No API. No shared RAM.
The only channel is: leave something in flash, then reset.
So "install this" has to be a mark in flash.
16 bytes, at the end of the download slot.
The application writes it; the bootloader reads it
after the next reset. That is the whole protocol.
1
"Downloaded" is not "wanted"
Download at 2 a.m., install during a
maintenance window. Two decisions,
two menu items: Download (2), then
Request installation (3).
2
It proves the download finished
Erased flash is 0xFF, and an aborted
transfer leaves a slot that looks like a
valid start. The magic sits AFTER the
image — so it exists only if all of it does.
3
Deliberately not a trust signal
The app writes it, so it can only say
"look here" — never "trust this".
Verification happens afterwards, and
rejects anything that fails.
the whole handshake
download the image
seconds to minutes
›
write 16 bytes
instant
›
reset
›
RoT verifies and installs
Without the flag the RoT would have to guess — re-verifying the download slot on every boot, or installing whatever happens to be lying there.
Notes: Answers the question the previous slide always provokes: why a separate 'request install' step at all. The short version: the two stages cannot talk, so the only channel is a mark in flash - and that mark also proves the download completed.

## Slide 11
Dual slot, SWAP — the device rescues itself
The old firmware is kept. The new one must prove it works, or it is put back automatically.
1
Download and request, exactly as before
PRIMARY SLOT
RUNNING
SECONDARY SLOT
STAGED — not trusted yet
MAGIC
2
Reset — the RoT verifies, then EXCHANGES the slots: the incoming image is decrypted, the outgoing one RE-ENCRYPTED
PRIMARY SLOT
NEW IMAGE
SECONDARY SLOT
PREVIOUS
3
The new firmware runs — on trial
it must write the confirmation flag at 0x8BFE0 — "I booted, keep me"
the last 32 bytes of the PRIMARY slot (0x8C000 − 0x20) — MCUboot's image_ok field; the final 16 bytes hold the trailer magic
the application writes one 16-byte programming unit there: 0x01 then zeros — FW_UPDATE_ValidAppImage(), menu "Validate app image"
Confirmed
the flag was written
PRIMARY
RUNNING
SECONDARY
PREVIOUS
the update sticks
Not confirmed
crash · hang · watchdog · power loss
PRIMARY
PREVIOUS, restored
SECONDARY
the failed one
the RoT swaps back by itself — no probe, no truck roll
Two marks, two slots: the magic trailer at the end of the SECONDARY slot asks for an install; the confirm flag at the end of the PRIMARY slot keeps what is now running.
Notes: The same flow plus one confirmation flag. Worth stressing: the confirm code already exists in our application, compiled out by OVERWRITE_ONLY.

## Slide 12
Bank swap (mirror) — move the map, not the firmware
One option-byte write instead of copying 464 KB. Install time drops to almost nothing.
SWAP_BANK = 0
BANK 1
RUNNING
BANK 2
NEW IMAGE
0x08000000
0x08080000
SWAP_BANK = 1
BANK 2
RUNNING
BANK 1
PREVIOUS
write one option byte
+ reset
What you gain
• install time ≈ 0 — nothing is copied
• revert is another flip, just as fast
• flash wear drops to almost nothing
The catch you must solve first
SWAP_BANK exchanges the WHOLE map — including 0x08000000,
where the immutable RoT itself lives. The bootloader moves too.
Usual answer: an identical, write-protected copy in both banks.
Status: not implemented in this repository — SWAP_BANK exists only as an option byte set to 0.
Notes: Attractive on paper - instant install. Be honest about the open question: SWAP_BANK moves the bootloader too, and nothing in our repo implements this yet.

## Slide 13
Bank swap — what you would actually have to mirror
The flip moves every address, so anything at a fixed address needs a copy in both banks
What needs a copy in both banks
Bootloader (RoT)
the flip moves 0x08000000, so whichever bank lands low needs a working RoT at offset 0
YES — two identical copies
Application
the two banks hold DIFFERENT images, new and old — that is the entire point
NO
Keys (pubkey hash, enc key)
they never change after provisioning, so the two copies stay identical
yes, harmlessly
NV counters (anti-rollback)
written at runtime, so the copies drift apart
yes — and that is a problem
Hash references
the inactive bank's cache does not match the image now running
yes, and they go stale
Calibration / config
the APPLICATION writes it, so a write after a flip lands in one bank only
yes, and worse
Install-request flag
no "secondary slot" to put a trailer at the end of
mechanism changes entirely
The mutable-state problem
Duplicating something that never changes is free.
Duplicating something written at runtime means the
two copies diverge — and after a flip you are looking
at the stale one.
For calibration that is an annoyance. For the anti-
rollback counter it is a SECURITY HOLE: flip to the
bank holding the older counter and the floor drops.
And it costs you application space
Dual-slot swap
~456 KB
one RoT, shared — 96 KB
Bank swap
~416 KB
two RoTs — 96 KB per bank
→ ~40 KB LESS for the application, not more.
Faster install · smaller application · harder to get right. Worth it only if install duration is a hard requirement.
There is no "outside the swapped region" to escape to either — SWAP_BANK exchanges the whole user flash. The realistic homes for device data are
external EEPROM or flash, or bank-aware addressing that always reaches the physical bank — if this part exposes such a view. Confirm in the reference manual.
Notes: The cost side of bank swap. Immutable things mirror harmlessly; runtime-written state (counters, calibration) does not - for the anti-rollback counter that is a security hole. And the doubled RoT leaves ~40 KB LESS for the application than dual-slot swap.

## Slide 14
Four ways to arrange the flash
Same bootloader (navy), same cryptography — only the slot strategy changes
SINGLE SLOT
no field update
APPLICATION
~925 KB for the app
a probe is the only way in
auto-revert
field update
no extra hardware
DUAL — OVERWRITE
runs today
PRIMARY
SECONDARY
~464 KB for the app
no way back from a bad image
auto-revert
field update
no extra hardware
DUAL — SWAP
auto-revert
PRIMARY
SECONDARY
~460 KB for the app
the old image is preserved
auto-revert
field update
no extra hardware
EXTERNAL DOWNLOAD
big app
APPLICATION
QSPI — SECONDARY
external component
~925 KB for the app
secondary slot lives on QSPI
auto-revert
field update
no extra hardware
The question that picks the column:
"If a correctly signed firmware installs, boots, and then fails — who rescues the device?"
The bootloader (swap) · a human with a probe (overwrite, single slot) · nobody (a locked device).
Notes: The four arrangements side by side. The closing question is the one that actually picks a column; everything else follows from it.

## Slide 15
Side by side
Green is where a choice costs you nothing — amber and red are where it bites
Single slot
Overwrite
Swap
Bank swap
External
Application budget
~925 KB
~464 KB
~460 KB
~460 KB
~925 KB
Install time
n/a
one copy
two copies
instant
copy + QSPI
Old firmware kept
no
no
yes
yes
no
Auto-revert on crash
no
no
yes
yes
no
App must confirm
no
no
yes
yes
no
Power-fail safe install
no
yes
yes
yes
yes
Extra hardware
no
no
no
no
QSPI chip
Status in this repo
not built
WORKS TODAY
app side ready
not implemented
driver only
"Works today" is the column the board boots from right now. Everything else is a decision, not a fact.
Notes: Detail view of the same trade-offs. The status row separates what we have from what we would have to build.

## Slide 16
What happens when an update goes wrong
Four of the five failures are handled identically — the fifth is the whole argument
OVERWRITE
SWAP / BANK SWAP
Forged or re-signed with the wrong key
rejected before install
rejected before install
Corrupted during the transfer
hash mismatch — rejected
hash mismatch — rejected
Genuine, but an old vulnerable version
below the counter — rejected
below the counter — rejected
Power lost during the install
the copy restarts
the swap resumes
Correctly signed — but it crashes at runtime
device stuck — needs a probe
reverts by itself, next boot
Signatures stop bad firmware. Only a second slot stops bad-but-genuine firmware.
Notes: The argument in one table. Four failures are handled identically - only the last row separates overwrite from swap.

## Slide 17
Six questions, in this order
Each answer removes whole branches — the last two cannot be changed after production
1
Is the firmware updated in the field at all?
no → single slot, and most of this is moot
2
If a signed firmware boots and then fails, must the device recover by itself?
yes → swap · no → overwrite
3
Does the application fit in ~464 KB?
no → external download slot, or revisit question 2
4
Is the firmware confidential?
no → drop encryption · yes → raw key or SAES-held key
5
What happens if the signing key leaks?
"we accept losing the fleet" — or design revocation NOW
IRREVERSIBLE
6
What is the production lock-down?
RDP level · tamper policy · dev mode off · regression allowed or not
IRREVERSIBLE
Where the answers land
P0
Lab — ships today
P1
No field update
P2
Production overwrite
P3
Safe update (swap)
P4
Big app (external)
P5
High assurance
Decide 5 and 6 first
They are listed last because the
earlier answers shape them —
but they must be settled before
the first device is provisioned.
After that, the bootloader and the
option bytes are locked forever.
Questions 1–4 are engineering. Questions 5–6 are commitments.
Notes: Proposed order for the decision. Questions 5 and 6 are irreversible once devices are provisioned, so they need an answer before anything ships.

## Slide 18
Questions that keep coming up (1/3)
The image format, and what the application is allowed to touch
What is the "magic trailer"?
A 16-byte flag the app writes at the very end of the download slot — "a candidate is ready".
• MCUboot's standard value, written at 0xFFFF0 in one flash programming unit (0x10 bytes)
• It sits AFTER the image data, so it can only be complete if the whole download was — power loss leaves no magic, and the RoT ignores the slot
• It is not a trust signal: the app writes it, so a forged one only makes the RoT verify and reject
secondary slot
0x8C000
image data, written front to back
MAGIC
16 B
0xFFFF0
The image arrives encrypted — should the app decrypt it before writing to flash?
No. Write it byte for byte, still encrypted. The application never decrypts anything.
• It could not anyway: the decryption key is at 0x12000, inside HDP, which closes before the app runs
• Decryption happens TWICE, both inside the RoT: once in RAM to reconstruct the hash the signature covers, once while copying into the primary slot
• Invariant: primary slot = clear, secondary slot = encrypted — visible in the two image recipes (-c vs -E)
• In swap mode the RoT re-encrypts the outgoing image on its way to the secondary slot
All the security is in the image format, not in the pipe — so the transport can be anything.
Notes: FAQ. The magic trailer is a completion flag, not a trust signal - and the app writes the image encrypted because it has no access to the key. Keep for questions.

## Slide 19
Questions that keep coming up (2/3)
Configuration and calibration data, and why it must live outside the slots
We keep calibration and configuration in flash. Must we mirror it into both slots?
No — move it OUT of the slots. The bootloader never touches anything outside them.
• Inside a slot it does not survive: overwrite erases the primary slot wholesale;
• swap carries the page out to the secondary slot, hands back a sector of the incoming image — and a revert undoes it again
• Mirroring inside the slots does not help; a dedicated region outside them does
today — the slots run to the top of flash, nothing is reserved
RoT + keys
PRIMARY 464 KB
SECONDARY 464 KB
one way to make room — 16 KB reserved, taken from both slots (data block not to scale)
RoT + keys
PRIMARY 456 KB
0x18000
SECONDARY 456 KB
0x8A000
DATA
16 KB
0xFC000
Swap needs equal slots
so N bytes of data area
costs 2N bytes of flash
Do not rewrite a struct in place
copy boot_nv_counters.c:
append + CRC, newest wins
Signed data shipped by you
is a different mechanism —
the data image (2 more slots)
Also: the primary slot spills 48 KB past the 0x80000 bank boundary — so "put the data in the other bank" needs a re-layout first.
Notes: FAQ. Calibration data must sit outside the slots; mirroring inside them does not work. Note the cost: reserving N bytes removes N from each slot.

## Slide 20
Questions that keep coming up (3/3)
What swap really costs, and what encryption does not cost
For swap, do we need two bootloaders? Do we mirror one bank into the other?
No to both. One bootloader, at 0x00000, never moved and never duplicated.
• Two different mechanisms share the word "swap" — this is the confusing part
• DUAL-SLOT SWAP: software exchanges the two SLOT CONTENTS. The RoT is not part of the move
• BANK SWAP (mirror): hardware flips the WHOLE address map — only THAT needs a second RoT, and its runtime-written state (counters, calibration) has no coherent home. It also leaves ~40 KB LESS for the app
• The running image is always in the primary slot, so it keeps today's link address: no relinking, no position-independent code
RoT
never moves, never copied
PRIMARY
the image that runs
SECONDARY
the previous image
contents exchanged
Does encryption slow the application down?
No. Zero runtime cost — the application executes plaintext from the primary slot.
• Before jumping, the RoT DISABLES AND RESETS the crypto clocks (RNG, SAES, HASH, PKA, CCB) — no crypto hardware is even running while your code does
• Decryption happens once, at install time, and is bounded by flash programming speed rather than by AES
• Boot time is driven by hashing the image and by ECDSA — which is exactly what the hash-reference cache exists to skip
• A runtime cost would appear only if you executed in place from encrypted EXTERNAL flash — not the case here
Encryption costs install time and a key to protect. It costs the application nothing.
Notes: FAQ. Two corrections worth stressing: swap needs ONE bootloader and no mirroring, and encryption costs the running application nothing.

## Slide 21
Open questions — for us, not for the datasheet
None of these are answered by the silicon or by the example. Each needs an owner and a date.
INTEGRATION & EFFORT
How hard is it to integrate this with
our existing FW updater?
What changes on the production line and
at end-of-line test?
How do we test updates at scale, and in
CI?
Who provisions the boards, and with
which tooling?
firmware · manufacturing
KEYS & PROCESS
Where is the signing key stored, and who
is allowed to use it?
One key for everything, or per product
line, per batch?
What is the plan if it leaks? Revocation
has to be designed in NOW
Who signs a release, and what approves
that signature?
security · IT
SCOPE & POLICY
Do we harden ALL next-gen devices, or
only some product lines?
Which RDP level ships — and does it
still allow RMA and failure analysis?
What is the recovery story for a device
that will not boot in the field?
Any certification driving this (PSA,
SESIP, CRA)?
product · support
Two of these close permanently at provisioning:
the key strategy and the lock-down level. Everything else can be revisited — those two cannot, because the bootloader is immutable.
Notes: Closing slide. Do not try to answer these here - the goal is to leave with an owner and a date against each. The key strategy and the lock-down level are the two that cannot be revisited after provisioning.